## Smart Agriculture IoT System

Senseed, a Smart Agriculture IoT System, is an end-to-end IoT solution designed to monitor and manage agricultural environments. This repository includes the firmware, hardware, enclosures, and server setup required to deploy the system.

System Overview
This system leverages a wireless sensor network in a star topology, using NRF24L01 modules operating at 2.4GHz for communication. The network comprises soil and environmental sensors that gather data and transmit it to a central gateway. The gateway serves as the primary hub, collecting sensor data and communicating with the controllers to make real-time adjustments.

For data processing and storage, the gateway connects to an Ubuntu server over WiFi, using the MQTT protocol with RabbitMQ as the message broker. On the server side, InfluxDB is used for time-series data storage.

The gateway is powered by an ATMEGA1284 and connects to the internet via an ESP32 module, utilizing AT commands. The sensors and controllers in the system are based on the ATMEGA328P microcontroller.
The environmental sensor is optimized for low-power operation, measuring temperature and humidity with a high-precision SHT40 sensor while also monitoring battery voltage to ensure reliable performance over extended periods.
The soil sensor assesses soil moisture levels using a moisture probe.
The controllers are designed for both low and high-power applications, managing devices through relay control. Each controller is equipped with a battery-powered real-time clock (RTC) to maintain accurate time in case of power outages. The high-power controller additionally monitors current consumption using an ACS712 sensor for enhanced energy management.

Smart IoT Framework for Landslide Monitoring in Coastal Areas
Developed a proof-of-concept end-to-end IoT solution for monitoring coastal landslides, integrating custom accelerometer sensors with a third-party LoRaWAN Gateway. The system leverages Chirpstack for network management and InfluxDB for data storage and visualization. Deployed on coastal cliffs in the UK, it successfully detected a landslide, providing geologists with critical insights and validating its operational effectiveness.

Smart Agriculture IoT System
Developed a prototype end-to-end IoT solution for agricultural monitoring, including custom PCBs designed for a gateway and battery-powered sensors and actuators. The system was optimized with low-power design techniques for a wireless sensor network (WSN) in a star topology. Backend components and a database schema were implemented on a Linux cloud server using InfluxDB and RabbitMQ.